## Slide 1
Young Kwan Kwon
New era of Nuclear Physics
with RI beams
2020.6.22~26
핵물리학교 @ on-line

## Slide 2
사업 개요 및 내용
01
사업 일반현황
1. 일반현황
사업개요 및 내용
CONTENTS
PART 0. NP with RIBs
PART 1. Project Overview
PART 2. Construction Status
PART 3. System Installation
PART 4. Radiation Safety
PART 5. Summary & Outlook

## Slide 3
Part 0.
NP with RIBs

## Slide 4: 30years anniversary for RIB’S
1. Introduction

## Slide 5: Experiments on nuclear physics
1. Introduction
A + B  C + D
beam
target
Until middle of 1980s, beam & target were stable nuclei

## Slide 6: Nuclear Physics with RIB’s: How it all started
1. Introduction
1966 at Lysekil, Sweden & 1970 at CERN, Switzerland
“Symposium on nuclei far from the stability”
Where is the neutron drip line?
Do the nuclear models which were successful for stable nuclei work also for n-rich nuclei?
The relevance to the r-process nucleosynthesis?

## Slide 7: The 1st exp with RIBs: neutron halo (I)
1. Introduction

## Slide 8: The 1st exp with RIBs: neutron halo (II)
1. Introduction
The 1st secondary beam line at Berkeley

## Slide 9: The 1st exp with RIBs: neutron halo (III)
1. Introduction

## Slide 10: Nuclear astrophysics with RIB’s (I)
1. Introduction
How are the chemical elements made ??
Unstable nuclei are playing a key role
: mass, reaction cross-section, beta decay life time etc…

## Slide 11: Nuclear astrophysics with RIB’s (II)
1. Introduction

## Slide 12: New magic numbers
1. Introduction

## Slide 13: Terra incognita in nuclear chart
1. Introduction
- Stable isotopes: ~ 300
- Unstable isotopes: ~ 3,000
- Unknown isotopes: 3,000~6,000

## Slide 14: RIB’s intensity
1. Introduction
Complexity
Identification
(in)elastic scattering
COULEX
breakup, knockout, ...
sR , ...
b-g, b-n
b (t 1/2 , Pxn)
invariant mass spectroscopy
Mass
transfer, charge exchange, ...
b-g-g, b-g-n, m ...
10/day
100/day
10/sec
1/sec
1/min
100/sec
103/sec
104/sec
~1/day

## Slide 15: ISOL vs IF
1. Introduction
IF(In-Flight methods)
Stable Heavy ion beam  thin target  projectile fragmentation, fission,
multi-nucleon transfer reaction, …
ISOL(Isotope Separator On-Line)
p  thick target (eg. Uranium Carbide)  target spallation or fission (low energy)
RI Ions
Reacceleration
RI ion beam
Stopping
RI Beam
Fast Beam
Experiment
Stopped Beam
Experiment
(Traps)

## Slide 16: RIB facilities in the world
1. Introduction
Slide from B. Sherrill
KISS (KEK-IPNS)
RIBs : Variety, Intensity, Energy, Purity

## Slide 17
Part 1.
RISP Overview

## Slide 18: Rare Isotope Science Project (RISP)
Providing high intensity RI beams by ISOL and IF
ISOL: direct fission of 238U by 70 MeV proton
IF: 200 MeV/u 238U (intensity: 8.3 pμA)
Providing high quality neutron-rich beams
e.g., 132Sn with up to 250 MeV/u,
up to 109 particles per second
Providing More exotic RI beam
production by combination of ISOL and IF
1. Overview
Budget: KRW 1,498 billion (US$ 1.23 billion, 1$=1,209krw)
- accelerators and experimental apparatus : 502.8 billion won
- civil engineering & conventional facilities : 996 billion won (incl. site 357 billion won)
Period: 2011.12 ~ 2021.12
Goal: To build a heavy ion accelerator complex RAON,
for rare isotope science research in Korea.
* RAON - Rare isotope Accelerator complex for ON-line experiments
Construction of research and support facility to ensure the stable operation of the heavy-ion accelerator, experiment systems, and to establish a comfortable research environment
※ Accelerator and experiment buildings, support facility, administrative buildings, and guest house, etc.
Development, installation, and commissioning of the accelerator systems that provides high-energy (200MeV/u) and high-power (400kW) heavy-ion beam
System Installation Project
Facility Construction Project

## Slide 19: RAON Layout
IF System
BIS
μSR
HPMMS/
CLS
SCL2
ISOL System
LAMPS
Cyclotron
SCL3
SCL1
ECR IS
KOBRA
NDPS
Control
Center
Utility
HRS
SCL1 has been decided to postpone
: SCL3 is going to be taking a role of SCL1 in the early operation
1. Overview

## Slide 20: RISP Organization
1. Overview
System Integration Division(21)
Project coordination Department(13)
Administration Division(14)
Experimental System Division(33)
Superconducting Technology Division(33)
Deputy Director
- HR & General
affairs Team
- Research Support
Team
- Procurement
Management Team
- Very Low Energy
Experimental System
Team
- Low Energy Experimental
System Team
- Intermediate Energy
Experimental System Team
- Beam Transport
Team
- Accelerator Control
Team
- Beam Physics Team
Facility Construction & Infrastructure Division(17)
Director
Quality Control Department(4)
- SCL Team
- RF Team
- Cryogenic System Team
- Superconducting Magnet
Team
- Construction Management
Team
- Facility & Safety
Management Team
- Project Policy and
Planning Team
- Project Management
Team

## Slide 21
RAON will provide access to unexplored regions of the nuclear chart
KOBRA
IF
ISOL
ISOL+IF
1. Overview
RIBs at RAON

## Slide 22
Project History
1. Overview
System Installation
Facility Construction
Project General
2012
2013
2014
2015
2016
2017
Jan 2012 Established Master Plan for RISP
June 2012 Submitted Basic Design Summary
(BDS)
June 2013 Completed Technical Design
Report (TDR)
Sep 2013 Revised the Master Plan (1st)
(period extension (~2019),
implementation schedule
change, etc.)
May 2014 Finalized the Master Plan for the
Establishment of the IBS
(Heavy-ion Accelerator)
July 2014 Finalized the Implementation Plan
for the Construction of the
Heavy-ion Accelerator Facility
Dec 2014 Began the basic design of facility
construction
April 2015 Revised the Master Plan (2nd)
(period extension (~2021),
implementation strategy
change, etc.)
Dec 2015 Completed the basic design
of facility construction
June 2016 Constructed the
SRF test facility
at Munji
Sep 2016 Started detail design
of facility construction
Feb 2017 Began the priority work of
facility construction
May 2017 Successfully completed
the performance test of the
SCL3 QWR module
June 2017 Completed the detail
design of facility
construction
Sep 2017 Began the facility
construction
Oct 2017 Successfully completed the
SCL demo runs
Dec 2017 Project review by TF
Jan 2009
Finalized the Comprehensive
Belt Plan (National Science &
Technology Commission)
June 2010
Completed the research to
establish the Heavy-ion
Accelerator Construction Plan
Feb 2011
Completed the Heavy-ion
Accelerator Conceptual Design
Dec 2011
Launched the Heavy-in
Accelerator Project
2018
March 2018
Completed
the SCL3 HWR
prototype module
performance test
2019
May 2019 Revised the Master Plan (3rd)
(scope and strategy change)
Sep 2019
Install the first QWR module

## Slide 23
2014
2015
2016
2017
2018
2019
2020
2021
SCL demo beam
(Dec 2017)
D-1
Experiment
(Jan 2021)
18.5MeV/u
SI beam
(Dec 2020)
SCL2
(Dec 2021)
ECR-IS beam &
ISOL beam (SI beam)
(Dec 2015)
RFQ beam
(Dec 2016)
System Installation
18.5MeV/u
RI beam
(Sep 2021)
SCL
installation
(April 2019)
ISOL
Commissioning
(July 2020)
Supply of utilities
(Dec 2018)
2014
2015
2016
2017
2018
2019
2020
2021
Completion of detail design
(June 2017)
Completion of construction
(Dec 2020)
Completion of inspection of the radiation facility
(Dec 2021)
Completion of basic design
(Dec 2015)
Beginning of priority
construction
(Feb 2017)
Beginning of construction
(Sep 2017)
Building
Permit
(April 2021)
Facility Construction
(2018)
SCL3 manufacturing
SCL2 Prototype
(2019)
SCL3 Installation
SCL2 manufacturing
(2020)
SCL3 Beam Commissioning/
Const. Completion
(2021)
KOBRA operation/
Project Completion
Project Milestone
1. Overview

## Slide 24
Progress Rate
1. Overview
Progress Rate
1. Overview
Chart: 
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Planned | 0 | 0.083 | 0.15 | 0.184 | 0.249 | 0.3046 | 0.42 | 0.6 | 0.78 | 0.91 | 1
Actual | 0 | 0.083 | 0.15 | 0.184 | 0.249 | 0.3014 | 0.407 | 0.5896 | 0.736
System Installation Project
As of May. 2020
(Planned: 83.20%,
Actual: 78.12%)
Construction Project
As of May. 2020
(Planned: 81.37%,
Actual: 81.40%)
Chart: 
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Planned | 0.0256 | 0.0367 | 0.1312 | 0.39 | 0.67 | 0.99 | 1
Actual | 0.0256 | 0.0367 | 0.1185 | 0.39 | 0.6743

## Slide 25
Part 2.
Construction

## Slide 26
Building Layout
2. Construction
Building Layout
Assembly Bd.
SRF Test Bd.
High Energy B
IF Separator / High Energy A
HQ Office
Guest House
Info. Center
Cryogenics Bd.
ISOL
SCL
Utility Bd.
Electricity Bd.
Control Center
Low Energy A,B
Waste Strorage
Reservation
Campus Area : 952,066㎡ (including the reservation area of 144,640㎡)
Period : 2014 ~ 2021(8 years)
Cost : 996 billion won (incl. 357 billion won for land)
Building Area : 76,259㎡(11 Bds)
Total Bd. Area : 116,252㎡
Constructor : POSCO Consortium(11 companies)

## Slide 27
Construction Schedule
2. Construction
Construction Schedule

## Slide 28
View of Construction Place
2. Construction
<`20.04>
<`17.01>
<`18.01>
<`19.01>
<Assembly Bd.>
<SRF Test Bd.>
<High Energy Exps.>
<ISOL>
<SCL3>
<Low Energy Exps.>
<Control Center>
View of Construction Place (`20.04)

## Slide 29
SCL3
Low Energy A/B
SCL2
IF/ High Energy A
High Energy B
ISOL
Conventional Facilities
2. Construction
Accelerator Bd.
SCL3
Bending Section
SCL3-gallery

## Slide 30
Assembly Bd.
Control Center
SRF Test Bd.
Utility Bd.
Electricity Bd.
HQ Office Bd.
2. Construction
Conventional Facilities

## Slide 31
Part 3.
System Installation

## Slide 32
Accelerator System
3. Sys. Install.
SCL3
(QWR)
SCL3
(HWR)
SCL2(SSR2)
KoBRA Beam Line
Injector
SCL2(SSR1)
Cyclotron
IF System

## Slide 33
Accelerator System
3. Sys. Install.

## Slide 34
Accelerator System
3. Sys. Install.

## Slide 35
Accelerator System
3. Sys. Install.
Until September `2020

## Slide 36
Accelerator System
3. Sys. Install.
Until September `2020

## Slide 37
Valve Box
Warm Section
QWR Cryomodule
Accelerator System-QWR unit
3. Sys. Install.

## Slide 38
MEBT
RFQ
LEBT
SC ECRIS
ECRIS
Accelerator System - Injector
3. Sys. Install.
∙ Two ECR ion sources on high voltage platforms
14.5 GHz ECR ion source
28 GHz superconducting ECR ion source
∙ LEBT (E = 10 keV/u)
Beam energy – 10 keV/u, Dual bending magnet
Chopper & Electrostatic quads, Instrumentation
∙ RFQ (E = 500 keV/u)
Frequency 81.25 MHz, Transmission Eff. ~98%
CW RF Power 94 kW (SSPA: 150 kW)
∙ MEBT (E = 500 keV/u)
Four RF bunchers (SSPA: 20, 15, 4×2 kW)
Simple quadrupole magnets, Instrumentation
SC ECRIS commissioning
RFQ commissioning
∙ RFQ has been conditioned to 40kW, sufficient to
accelerate A/q=4.5 beams
Output Energy of RFQ(TOF)
~508keV/u
Amplitude control of RFQ
RFQ
QWR CM
ECRIS
∙ Beam experiment for the performance enhancement
∙ Basic metal beam experiment
Ar beam experiment
Charge distribution
Ar 11+ 70uA
Injector

## Slide 39
Accelerator System – SCL3
3. Sys. Install.
SCL31(QWR)
∙ Design performance was achieved with prototypes(2017.5)
∙ Oxygen beam was accelerated with injector and one QWR module(2017.10)
500 keV/u  ~700 keV/u, Successful long-tem operation of cryomdoule
∙ Mass production was contracted with domestic vendor(2017.12)
Pre-production cavities and cryomodules passed qualification, mass production is on-going
Total thermal load <20W@6.1MV/m, 4.2 K
SCL32(HWR)
∙ Design performance was achieved with prototypes(2017.10)
Thermal load <14.1W@6.6MV/m, 2.1 K (HWR type A)
∙ Mass production was contracted with domestic vendor(2018.5)
∙ SSPA (4kW) : 2018.07~2020.05
Pre-production performance test(2019.11)
∙ HPRF transmission line (1-5/8”)
Installation vertical parts (2019.10)
∙ LLRF control system (2019.07~2020.06)
∙ RF reference line (81.25MHz) : ~2019.12
QWR
HWR#A
HWR#B
RF System
VT target: 2.4e+8@6.1MV/m
Static thermal load: 5.8 W
(Target: max. 7.5 W)

## Slide 40
VT target: 2.4e+8 at 6.1 MV/m
Accelerator System – QWR
3. Sys. Install.

## Slide 41
VT target: 2.3e+9 at 6.6 MV/m
Accelerator System – HWR
3. Sys. Install.

## Slide 42
CM-#2
CM-#5
 | Total (W) | Static (W) | Dynamic (W) | Q0 of cavity
QWR-CM-#1 | 11.7 | 7.7 | 4.0 | 6.0e+8
QWR-CM-#2 | 10.8 | 8.0 | 2.8 | 8.5e+8
QWR-CM-#3 | 13.1 | 8.4 | 4.7 | 5.1e+8
QWR-CM-#5 | 14.4 | 9.5 | 3.5 | 6.6e+8
All tested cryomodules meet the total thermal load requirement (20 W) though the cryomodules did not thermalized.
NO significant performance degradation of cavities during cryomodule assembly.
Accelerator System – QWR HT
3. Sys. Install.

## Slide 43
Accelerator System – SCL2
3. Sys. Install.
SCL21(SSR1)
∙ 1st prototype was performed by TRIUMF(2019.6)
Balloon type(less multipacting, better mechanical characteristics)
Accelerating gradient over 8.7MV/m, Multipacting below 2MV/m
∙ 2nd prototype with domestic vendor is on-going
2nd prototype by domestic vendor
SCL22(SSR2)
∙ 1st prototype of cavity is on-going
Designed by RISP, fabricated by domestic vendor
Balloon type, Deep drawing (depth ~280mm)
∙ 2nd prototype with IHEP is on-going
Cylindrical type
RISP design(balloon type)
1st prototype by TRIUMF
∙ SSPA (8, 20 kW): 2020.01~2021.06
Requirement for RF power rating
∙ HPRF transmission line
3-1/8”, 4-1/16” rigid coaxial
∙ LLRF control system (2020.04~2021.06)
∙ RF reference line (81.25MHz) : ~2020.12
SSR1
SSPA Prototype
RF System

## Slide 44
Major achievements in R&D
3. Sys. Install.
ECR IS
LEBT
RFQ
MEBT
QWR
Superconducting RF Test facility(2016.06)
High purity Sn beam extraction
using RILIS (2015.12)
1st Oxygen Ion beam acceleration with a QWR module, SCL Demo(2017.10)
HWR cryomodule test complete
(2018.03)
QWR cryomodule test complete
(2017.05)
1st Oxygen Ion beam acceleration with RFQ(2016.12)
Achievement of low temperature test for LTS and HTS quadrupole prototype magnet (LTS 2017.11, HTS 2017.2)

## Slide 45
Beam Physics
3. Sys. Install.
Start-to-end simulation: uranium (238U33+,34+→77+,78+,79+,80+,81+)
SCL3
SCL2
Physics application tools
BIPAM (Beam Input Parameter And Matching)
CAPS (Cavity Amplitude and Phase Scan)
SCL2 extension
On-line orbit correction
Transverse beam size
Longitudinal beam size

## Slide 46
Injector beam commissioning
  Period: 2020. 03 2020. 09
  Section: 14.5 GHz ECR-IS → LEBT → RFQ → MEBT
  Reference beam: 40Ar9+ or O (50 ms pulse beam, 1Hz repetition rate)
14.5 GHz ECR-IS
LEBT
RFQ
MEBT
LEBT
  Charge selection
  Emittance measurement beam distribution regeneration
  Transverse beam size measurement
  Orbit correction
  Pencil beam test, etc.
RFQ
  Beam transmission
  Beam energy measurement, etc.
MEBT
  Rebuncher amplitude & phase scan
  Transverse beam matching
  Longitudinal beam matching
  Orbit correction, etc.
Beam Physics
3. Sys. Install.

## Slide 47
Control System
3. Sys. Install.
Control Center
Main Control Room
Data Storage System
Local Control System
Beam Diagnostics Control System
Integrated Control System
Fast Protection System
EPICS IOC
Controllers
SCL3 Control System(43)
Timing System

## Slide 48: SCL3 Warm Section – Chamber and magnets
Diagnostic chamber
∙ 15 sets were already fabricated.
- BPMs, Wire scanners and Faraday cups
∙ Need to assemble in the clean condition
Vacuum chamber
3. Sys. Install.
∙ 53 sets were are already fabricated.
- NEG pumps and gauges
∙ Need to assemble in the clean condition
Magnets

## Slide 49
Installation Procedure
3. Sys. Install.
Alignment network Survey (2019. 4 ~ )
Transportation to the accelerator building

## Slide 50
Installation Procedure
Warm section assembly
class 100
Rinse
Dry
Assemble
Leak check
Conditioning
class 10
class 100
(150℃, 120h)
3. Sys. Install.

## Slide 51
Installation Procedure
Cryomodule + Warm section
∙ Assemble in front of the tunnel (ISOL building)
∙ 15-ton crane is available.
∙ Need to connect between cryomodule and warm section in the clean condition
3. Sys. Install.

## Slide 52
Installation Procedure
Transport and positioning in the tunnel
∙ To prevent alignment change due to vibration
∙ To transport 10-ton HWR-B cryomodul in the tunnel
∙ For fine positioning
Impossible to use wheels
Adopting air caster
3. Sys. Install.

## Slide 53
Installation Procedure
Launching celebration of the 1st QWR cryomodule installation
3. Sys. Install.

## Slide 54
Installation Procedure
(Cryomodule + Warm section) + (Cryomodule + Warm section)
∙ At least one port should be assembled in the tunnel
∙ Difficult to make clean conditions due to the tight space
∙ Design a simple clean booth is underway
3. Sys. Install.

## Slide 55
Control System
3. Sys. Install.
Control Center
15m
Display Wall
Data Storage System
Local Control System
SCL3 Control System
Embedded EPICS IOC Controller
Beam Diagnostics Control System
Integrated Control System
Timing System
Fast Protection System

## Slide 56
RI & Experimental System
3. Sys. Install.
Low Energy Exp. Bldg
Ultra-low Exp. Bldg
High Energy Exp. Bldg
CLS
HPMMS
Neutron Facility
KOBRA
mSR
LAMPS
ISOL
IF
Bio-medical facility

## Slide 57
Cryogenic System
3. Sys. Install.
Tasks | 2019 |  |  |  |  |  |  | 2020 |  |  |  |  |  |  |  |  |  |  |  | 
 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1
SCL3 Cryoplant (4.2 kW) SCL2 Cryoplant (13.4 kW) Cryogenic Distribution System (SCL3) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Fabrication (QWR)
Installation and Inspection
Installation (transfer line)
Installation (valve boxes)
Fabrication
(HWR and transfer line)
Commissioning
Inspection
and connection with cold box
Design and Fabrication
Installation & Inspection
Now
Prototype test
SCL3 Cold Box (95 ton)
SCL2 Cold Box (130 ton)
QWR Valve Box
(Prototype and installation test)
SCL3 Commissioning
19.5 m
15 m
Connection
( Valve Box – Cryomodule )
Design and Fabrication
Commissioning

## Slide 58
ISOL system
3. Sys. Install.
Line 2
Line 1
Bunker-L
Bunker-R
TIS-L
TIS-R
pre-mass separator room L
pre-mass separator room R
RFQ-c/b + EBIS
A/Q separator line
MMS
Branch point
HRMS
TIS.L Pre-sep  HRMS  user
TIS.R Pre-sep.  Mass sep.  HRMS  user
TIS Pre-sep.  HRMS  EBIS  a/qpost acc.
Test Facil. (low pow., non U)  Pre-sep  user
Now concentrating on the shortest line
TIS.L  Pre.sep  EBIS  A/q  Post.acc
ISOL building ready by ‘19.12
- Ground floor: TIS, beamline,
experimental hall
- 1st floor: experimental hall, Laboratory, utilities
- 2nd floor: Control room, Analysis room
Early stage operation

## Slide 59
IF system
3. Sys. Install.
In-Flight separator layout

## Slide 60
Nuclear science - KOBRA, LAMPS, NDPS, MMS, CLS (based on atomic physics)
Applied science - mSR (Material science), BIS (Bio & Medical application)
7 (at the beginning of RAON operation) + upgrade + a (in the future, space reserved)
3. Sys. Install.
Layout of Experimental System at RAON

## Slide 61
1. KOBRA
(KOrea Broad acceptance Recoil spectrometer & Apparatus)
2. LAMPS
(Large Acceptance Multi-Purpose Spectrometer)
∙ Research Studies of nuclear structure and nuclear
astrophysics in the energy range of < a few tens of MeV/u
∙ Current status Under fabrication (start installation from Sep. 2019)
∙ Research Studies of nuclear matter and nuclear reactions
with stable and RI beams at intermediate energy regime
∙ Current status Under fabrication (start installation from Jan. 2021)
IF separator
3. ACC. & Exp.
3. Sys. Install.
Current Status of Experimental System

## Slide 62
3. MMS (Mass Measurement System)
∙ Research High precision mass measurement of
short lived rare isotopes
∙ Current status Under assembly and test
(start installation from Feb. 2020)
MR-TOF-MS
4. CLS (Collinear Laser Spectrometer)
∙ Research Model independent Studies of
nuclear ground and isomeric state properties
∙ Current status Restart development
(start installation from Jan. 2020)
5. NDPS (Neutron Data Production System)
∙ Research Measurement of neutron
induced reaction data for nuclear science
∙ Current status Restart development
6. mSR (Muon Spin Rotation/Relaxation/Resonance )
∙ Research Studies of local electromagnetic structures and
exotic properties of material by using polarized muons
∙ Current status Restart development
7. BIS (Beam Irradiation System)
∙ Research Biomedical studies such as cancer treatment,
human body effect by space radiation and cell mutation
∙ Current status Restart development
(start installation from Jan. 2021)
(start installation from Nov. 2020)
(start installation from Feb. 2021)
3. ACC. & Exp.
3. Sys. Install.
Current Status of Experimental System

## Slide 63
KOBRA
3. Sys. Install.
Low energy experimental hall B
Low energy experimental hall A
ISOL facility
SCL1
IF facility
High energy experimental hall A
High energy experimental hall B
KoBRA
Goal: Construction of multi-purpose experimental instrument using stable or RI beams for studies of the nuclear structure and nuclear astrophysics, in the energy range of about 1 – 30 MeV/u
RI beam productions at a few MeV/u and at about 20 – 40 MeV/u using a stable beams from ECR ion source
Recoil mass separator at less than few MeV/u for direct measurements of radiative-capture cross, using a RI beams from ISOL facility
SCL3
SCL2
Ions are accelerated
up to about 40 MeV/u for A < 40,
up to about 20 MeV/u for A > 100
Spallation room for future extension
2018.08

## Slide 64
KOBRA
3. Sys. Install.
Contracted on April 2018
((Korea)
Productions of quadrupole and sextupole magnets
(Denmark)
Project management
Designs of all magnets
Productions of bending magnets and swinger
((Korea)
Project management
Consortium
(Korea)
Designs and productions of diagnostic chambers, beam pipe, beam dump, and etc.
Small quadrupole magnet
Swinger
Sextupole magnet
F1 chamber
F2 chamber
F3 chamber
F0
F1
F2
F3
Wien Filter will be added later
Contracted on Dec 2018
Removable scattering chamber
Empty space for Si-detector array
or IC chamber
5 m

## Slide 65
KOBRA
3. Sys. Install.
• All of detectors are fulfilled KoBRA detection system requirements
• Complete KOBRA detection system including spare detectors, Ion Chamber, HPGe gamma array and DAQ system will be
ready by the middle of 2019
PPACs
• Six 10 x 10 cm2, two 20 x 20 cm2, two 40 x 20 cm2 active area PPACs
• Position resolution: < 1 mm in FWHM, (C4H10 gas, 16O beam at 2x106 pps)
SSD
• Two 5 x 5 cm2 active area, 50 m-thick, 16 channel SSD
• Energy resolution ~ 0.7%, S/N ~ 272 for 5.486 MeV  in vacuum
Plastic scintillator detectors
• One 10 x 10 cm2 active area, 100 m thick both side readout plastic detector
• One 10 x 10 cm2 active area, 100 m thick one side readout plastic detector
• Time resolution < 42 ps for 5.486 MeV  in vacuum
HPGe gamma ray detectors
• 32 segmented HPGe detectors (6set)
• Compton suppressor BGO crystals (6set)
• Complete set of TIGRESS electronics
Large area PPACs
PPACs
SSD
HPGe gamma array
Use B-ToF-∆E technique for RI identification

## Slide 66
LAMPS
3. Sys. Install.
Main facility for nuclear matter and nuclear reaction studies with stable and rare isotope beams at intermediate energy
• Main Research Subject
Study of nuclear symmetry energy at supra-saturation density via heavy-ion collision experiment using rare isotope beam with varying beam energies and collision systems
(e.g. measure n/p ratio & collective flow at the same time in the combination of 50,54Ca+40Ca, 68,70,72Ni + 58Ni,
106,112,124,130,132Sn + 112,118,124Sn)
▪ Beam Energy: up to 250 MeV/u for 132Sn (≤ 108 pps)
▪ Solenoid Spectrometer
- Max. 1T solenoid magnet
- TPC (~ 3 sr acceptance, charged particle tracking)
- Scintillation counter (trigger & ToF)
▪ Neutron Wall (neutron tracking)
IF separator

## Slide 67
LAMPS
3. Sys. Install.
Fine tuning on the design parameters by experts
  Cylindrical SC magnet
  Dim.: 3300 mm (L) 2200 (W) 2600 mm (H)
  Fit into the pit
  Diameter of bore = 1600 mm
  Max. -field > 1 T
  Variation of -field over TPC volume = ±0.94%
  Passive quench protection
  Conduction cooled with 4K vessel thermal shield and vacuum vessel
Contracted with Tesla Engineering Ltd. UK by RISP magnet⁃vacuum R&D group in Feb. 27, 2019
Production design is ongoing

## Slide 68
LAMPS
3. Sys. Install.
Drift length = 1200 mm
Final design of readout, gas vessel, and field cage is in progress
  Readout will be only at the upstream end
  P20 gas with > 6 cm/µs meets entire readout time of GET electronics over full drift length (120 cm)
  Octagonal outer barrel and circular inner barrel
  Inner radius: 150→100 mm, Outer radius: 500→535 mm
  Maximize the active region for R = 105 ~ 503.5 mm
Test of the real-size GEM foil is underway
  If gain is too small, an option for quadruple GEMs may be explored
LAMPS TPC will be constructed in 2019 and tested by 2020
Pad dim.: ~ 310 mm2
# of Ch.: 2,618/sector 8 sectors = 20,944
FEE: 11 AsAD/sector 8 sectors = 88 AsAD

## Slide 69
LAMPS
3. Sys. Install.
Installation of all modules (160 neutron detectors + 20 veto detectors) in the frame were completed in December, 2018
Preparation of cosmic muon test is almost ready
Detector operation will be done remotely at Korea University Lab. in Seoul

## Slide 70
MR-TOF
3. Sys. Install.
Low energy beam of < 60 keV
Differential pumping stage
Windowless helium gas catcher
Trap and bunching system
MRTOF reflection chamber
Connection with CLS is now on the discussion

## Slide 71
MR-TOF
3. Sys. Install.
“Fast and Precise”
Mass measurement, but also Beam purification
Mirror electrodes
1: mass of interest
2: mass of reference
MR-ToF-MS can provide a high mass resolving power of > 105 even with short measurement time of 10 ~ 30 msec
It is more suitable for the short-lived nuclei region

## Slide 72: Scientific program at early phase operation(candidate)
Facility | Subject for early phase operation
KOBRA | ∙ Transfer reaction measurements in inverse kinematics (29P(d,p)30P, 26Al(a,p)24Si) ∙ Radiative capture reactions using batch mode RI beams (26gAl(p,g)27Si) ∙ RI beam production via quasi-projectile-like fragmentation for 16O or 40Ar
LAMPS | ∙ Ar+KCl or Xe+CsI in case of IF separator commissioning not completed
MMS | ∙ Isomer separation with using 26g.s.Al and 26mAl beams
CLS | ∙ Laser ionization and measurement of isomeric property for 26Al
NDPS | ∙ Activation experiments with a quasi mono energy neutrons for light and heavy nuclei ∙ Surrogate reactions for fission
mSR | ∙ One of research areas of superconductivity and quantum magnetism with their scientific significance at the time of the μSR instrument completion
BIS | ∙ Physical dose distribution and linear energy transfer measurements with a 12C+6 beam (310 MeV/u)
3. Sys. Install.

## Slide 73
International Cooperation (MOUs with 18 Intl Institutes)
3. Sys. Install.
27

## Slide 74
Part 4.
Radiation Safety

## Slide 75
Radiological Features of the Facility
4. Rad. Safety
High Power Targets
Use of Uranium Material
Various Reactions to analyse
various beam and target combination
wide energy range (low 18~40MeV/u, high 200~320 MeV/u, 600 MeV p)
need to find correct simulation codes and conditions
IF : 400 kW, ISOL : 30 ~ 70 kW
induce high activation in concrete, air, cooling water, machine parts
need robust remote handling in target areas
fission products contaminate ISOL target system, IF beam dump, etc.
generation of radioactive waste containing actinides-> need a long-term storage space of the waste until ready to transfer to the national site
Experiments | Beams | Targets
IF | O, Ca, …, Kr, .., Sn, Xe, U, ~20 species | C
ISOL | p | UC
KOBRA | He, B, O, Ar, U | Be, Cu
Bio-medical | C | Fe
muSR | P | C
LAMPS | Ca, Ni, Zr, Sn | Ca,….
Neutron Exp. | p, d | C

## Slide 76
Radiation Safety Licensing : Completed!! (18.10)
Preparation
many domestic experts joined radiological analysis
facility basic design by a experienced company
Documents for Review
radiation safety report
(shielding, activation, env. Influence, RMS/PSIS,
exhaust, accident analysis, radioactive waste, etc..)
description of accelerators and experiments
details in radiological analysis (codes, input/output)
geological survey report
stability assessment of building and ground
quality assurance plan/procedures
fire hazard analysis
Extensive Reviews
NSSC
(Nuclear Safety and Security Commission)
KINS
(Korea Institute of Nuclear Safety)
License Submission
& Approval
Technical Review Request
& Review Report
Technical Detail
Inquiry & Answer
RISP
by more than 30 KINS reviewers
382 cases of answers/further assessment/correction/design improve and changes
multilevel review(KINS, NSSC, Advs..)
4. Rad. Safety

## Slide 77
Plan – First Facility Inspection
mandatory step before operation (every year after the first inpection)
check items
safety organization / manpower
record of quality assurance activity
performance of all RMS & PSIS systems
implementation of fire protection
performance of exhaust/draining/remote system
readiness of preventive and mitigative measures for possible accidents of more once in 30 years
procedures to handle radioactive wastes
etc..
’19 |  |  |  | ‘20 |  |  |  | ‘21 |  |  | 
1Q | 2Q | 3Q | 4Q | 1Q | 2Q | 3Q | 4Q | 1Q | 2Q | 3Q | 4Q
Arranged with KINS
to make 3-steps inspection
Ion Source,
Injector
SCL3, KOBRA
ISOL,SCL2+IF, h.e.Exps
Safe Facility for workers & vistors & citizens !
RMS Equipments in the site | 
Environment Monitor | 12
Area Monitor | 94
Area Air Monitor | 11
Stack Monitor | 6
Hand & Foot Monitor | 11
Nuclide Analyser | 6
Paging Phone | 88
CCTV camera | 101
Emergency Stop & Alarm | 174
Vehicle Radiation Monitor | 2
4. Rad. Safety

## Slide 78
Part 5.
Summary & Outlook

## Slide 79
Accelerator
Mass production for SCL3 is under way and SCL2 is under pre-production stage.
Beam commissioning for the injector begins in the spring 2020.
From April, 2019, installation for SCL3 has been started and will completed by the end of 2020.
By the end of 2021, we will achieve
SI beams: Stable ion beams (16O, 40Ar) from ECRIS  SCL3  low E exp hall
RI beams: RIBs extraction from ISOL  re-acceleration through SLC3  low E exp hall
Stable / RI beams will be delivered to low-E experimental hall
Early phase experiments are going to be performed using KOBRA
  RIBs production at KOBRA (A<~50, beam energy < 20 MeV/u) using SI beams from SCL3
Beam commissioning begins for SCL2
Installation and commissioning for IF, LAMPS, Neutron, bio-medical and mSR
   Collaborative works with RUA (RAON Users Association) via RULC (RAON Users Liason Center)
Post RISP (2021 ~ )
Beam acceleration for ISOL  SCL3  SCL2  IF (ISOL+IF)
Beam commissioning and experiments for IF, LAMPS, Neutron, bio-medical and mSR
Ramping-up to get the 400kW beams (more than 5 yrs)
Energy upgrade to 400MeV/u (requires budget)
Summary & Outlook
4. Summary

## Slide 80
Thank you

## Slide 81
Backup slides

## Slide 82
ISOL system
Sys. Install.
Temperature of the target
Temperature of the chamber
Thermal stress of the target
Proton Beam | 
Energy | 70 MeV
Power | 10 kW
Beam size | 45 mm
Target | 
Material | UCx
Density | 2.5 g/cm3
U weight | 101 g
# of disk | 19
Disk thickness | 1.3 mm
Disk diameter | 50 mm
Total length | 22 cm
Release time of 132Sn
Temperature distribution
In-target fission rate
Maximum thermal stress
Expected In-target fission rate
= 1.6×1013/s
benchmarking SPES 8 kW target system
10 kW Ucx target system design

## Slide 83
ISOL system
Ion beam extraction experiment
SIS: Cs and Rb ion beam extraction
RILIS: Sn ion beam extraction
Ionization efficiency measurement
Mass resolving power M/ΔM > 400
Emittance measurement
ISOL Test Facility
Sys. Install.

## Slide 84
ISOL system
Hot cell : TIS replace, maintenance
- four manipulator, two module driving system, TIS exchange device
- TIS chamber insert to pail and the pail move to storage
Remote crane for module & TIS transfer
- three hoist : 20 ton(module transfer & shield block removal) / 7 ton(TIS pail transfer) / 7 ton(maintenance)
- position accuracy : < 5 mm
On manufacturing
< Remote crane & interface system >
< Hot cell & remote handling system >
Sys. Install.

## Slide 85
E-gun/Collector
Ion trap region
SC solenoid (6T)
Ion transport line
Test ion source (Cs1+)
Alignment and Assembly of RAON EBIS
Sys. Install.

## Slide 86
52nd shot
Collector
Cathode
Apertures
 Magnetic Field : 2T
 Cathode voltage: -5.5kV → -6kV
 Cathode heater: 85W
 Gun coil: 200 → 170A, Collector Coil: 130 → 140 A
 52nd Shot: 516mA → 416mA (81%) @ Vpp = 9.5kV
 Collector conditioning with 3 Hz
Alignment and Assembly of RAON EBIS
Sys. Install.
EBIS short pulse(10us) e-beam extraction experiment

## Slide 87
ISOL system
Remote Handling
Hot Cell
TIS Bunker/Module
RH Mock-up
Sys. Install.

## Slide 88
IF system
Magnet to be combined with IF slide
Sys. Install.

## Slide 89
MR-TOF
Differential pumping section : 450L/sec x 2, two rooms (w/ ⌀ 8 mm aperture)
Gas catcher : ⌀2 mm aperture, ⌀190 mm x 250 mm (cylindrical), RF carpet + DC cylinder
Triplet trap system : Linear Paul trap x 2, Flat trap x 1
MRTOF analyzer : Au-plated Al electrodes (18), 520 mm (including base)
Others : quadrupole ion guide, channeltrons x 3, IS x 2
Performance test for individual parts is completed
Tuning of total system is ongoing
Sys. Install.