## Slide 2: Rare Isotope Science Project (RISP)
Providing high intensity RI beams by ISOL and IF
ISOL: direct fission of 238U by 70 MeV proton
IF: 200 MeV/u 238U (intensity: 8.3 pμA)
Providing high quality neutron-rich beams
e.g., 132Sn with up to 250 MeV/u,
up to 109 particles per second
Providing More exotic RI beam
production by combination of ISOL and IF
1. Overview
Budget: KRW 1,498 billion (US$ 1.23 billion, 1$=1,209krw)
- accelerators and experimental apparatus : 502.8 billion won
- civil engineering & conventional facilities : 996 billion won (incl. site 357 billion won)
Period: 2011.12 ~ 2021.12
Goal: To build a heavy ion accelerator complex RAON,
for rare isotope science research in Korea.
* RAON - Rare isotope Accelerator complex for ON-line experiments
Construction of research and support facility to ensure the stable operation of the heavy-ion accelerator, experiment systems, and to establish a comfortable research environment
※ Accelerator and experiment buildings, support facility, administrative buildings, and guest house, etc.
Development, installation, and commissioning of the accelerator systems that provides high-energy (200MeV/u) and high-power (400kW) heavy-ion beam
System Installation Project
Facility Construction Project

## Slide 3: RAON Layout
IF System
BIS
μSR
HPMMS/
CLS
SCL2
ISOL System
LAMPS
Cyclotron
SCL3
SCL1
ECR IS
KOBRA
NDPS
Control
Center
Utility
HRS
SCL1 has been decided to postpone
: SCL3 is going to be taking a role of SCL1 in the early operation
1. Overview

## Slide 4
RAON will provide access to unexplored regions of the nuclear chart
KOBRA
IF
ISOL
ISOL+IF
1. Overview
RIBs at RAON

## Slide 5
Project History
1. Overview
System Installation
Facility Construction
Project General
2012
2013
2014
2015
2016
2017
Jan 2012 Established Master Plan for RISP
June 2012 Submitted Basic Design Summary
(BDS)
June 2013 Completed Technical Design
Report (TDR)
Sep 2013 Revised the Master Plan (1st)
(period extension (~2019),
implementation schedule
change, etc.)
May 2014 Finalized the Master Plan for the
Establishment of the IBS
(Heavy-ion Accelerator)
July 2014 Finalized the Implementation Plan
for the Construction of the
Heavy-ion Accelerator Facility
Dec 2014 Began the basic design of facility
construction
April 2015 Revised the Master Plan (2nd)
(period extension (~2021),
implementation strategy
change, etc.)
Dec 2015 Completed the basic design
of facility construction
June 2016 Constructed the
SRF test facility
at Munji
Sep 2016 Started detail design
of facility construction
Feb 2017 Began the priority work of
facility construction
May 2017 Successfully completed
the performance test of the
SCL3 QWR module
June 2017 Completed the detail
design of facility
construction
Sep 2017 Began the facility
construction
Oct 2017 Successfully completed the
SCL demo runs
Dec 2017 Project review by TF
Jan 2009
Finalized the Comprehensive
Belt Plan (National Science &
Technology Commission)
June 2010
Completed the research to
establish the Heavy-ion
Accelerator Construction Plan
Feb 2011
Completed the Heavy-ion
Accelerator Conceptual Design
Dec 2011
Launched the Heavy-in
Accelerator Project
2018
March 2018
Completed
the SCL3 HWR
prototype module
performance test
2019
May 2019 Revised the Master Plan (3rd)
(scope and strategy change)
Sep 2019
Install the first QWR module

## Slide 6
2014
2015
2016
2017
2018
2019
2020
2021
SCL demo beam
(Dec 2017)
D-1
Experiment
(Jan 2021)
18.5MeV/u
SI beam
(Dec 2020)
SCL2
(Dec 2021)
ECR-IS beam &
ISOL beam (SI beam)
(Dec 2015)
RFQ beam
(Dec 2016)
System Installation
18.5MeV/u
RI beam
(Sep 2021)
SCL
installation
(April 2019)
ISOL
Commissioning
(July 2020)
Supply of utilities
(Dec 2018)
2014
2015
2016
2017
2018
2019
2020
2021
Completion of detail design
(June 2017)
Completion of construction
(Dec 2020)
Completion of inspection of the radiation facility
(Dec 2021)
Completion of basic design
(Dec 2015)
Beginning of priority
construction
(Feb 2017)
Beginning of construction
(Sep 2017)
Building
Permit
(April 2021)
Facility Construction
(2018)
SCL3 manufacturing
SCL2 Prototype
(2019)
SCL3 Installation
SCL2 manufacturing
(2020)
SCL3 Beam Commissioning/
Const. Completion
(2021)
KOBRA operation/
Project Completion
Project Milestone
1. Overview

## Slide 7
Low energy experimental hall B
Low energy experimental hall A
ISOL facility
SCL1
IF facility
High energy experimental hall A
High energy experimental hall B
Korea Broad acceptance Recoil spectrometer and Apparatus
KoBRA
Goal: Construction of multi-purpose experimental instrument using stable or RI beams for studies of the nuclear structure and nuclear astrophysics, in the energy range of about 1 – 30 MeV/u
RI beam productions at a few MeV/u and at about 20 – 40 MeV/u using a stable beams from ECR ion source
Recoil mass separator at less than few MeV/u for direct measurements of radiative-capture cross, using a RI beams from ISOL facility
SCL3
SCL2
Ions are accelerated
up to about 40 MeV/u for A < 40, up to about 20 MeV/u for A > 100
Spallation room for future extension
2018.08

## Slide 8
가스 또는 금속 샘플 주입
(안정 원소: 안정한 원자핵)
+
+
+
+
+
+
이온원 (ion source)
가속관
입사빔 (1차 빔, Primary beam or Projectile)
이온화
전자석
생성 표적 (production target)
+
+
+
반응하지 않고 지나가는 1차 빔
Projectile
Target
Excited projectile-like fragment
De-excitation of fragment
fragmentation
Projectile-like fragmentation
표적과 반응하여 생성된 희귀동위원소 (RI)
(2차 빔: Secondary beam or fragments)
Basics of RI production: 희귀동위원소(RI) 빔 생성 (in-flight method)

## Slide 9
가스 또는 금속 샘플 주입
(안정 원소: 안정한 원자핵)
+
+
+
+
+
+
이원온(ion source)
가속관
이온화
전자석
생성 표적 (production target)
+
+
+
원하는 희귀동위원소를 어떻게 식별하고 (분리하여) 빔으로 사용할 것인가?
Basics of RI production: 희귀동위원소(RI) 빔 생성 (in-flight method)
표적과 반응하여 생성된 희귀동위원소 (RI)
(2차 빔: Secondary beam or fragments)
반응하지 않고 지나가는 1차 빔
입사빔 (1차 빔, Primary beam or Projectile)

## Slide 10
RI beam
Primary beam
Beam dump
Production target
Slit
Slit
Bending magnet
Bending magnet
Momentum dispersive focal plane
Position measurement
Energy loss/Time-of-flight measurements
Momentum dispersive focal plane
Achromatic focal plane
Lorentz force: F = qvB
Centripetal force: F = mv2/ρ
mv/q = Bρ ~ horizontal position
Velocity v = Flight length / TOF
Nuclear charge Z ~ ΔE1/2 v
Achromatic focal plane
Position measurement → determine mv/q
Position and TOF measurements → determine A/q
Energy loss/Time-of-flight measurements → determine Z
Bρ- ΔE-TOF method
Basics of Separator : 2차 빔 분리 장치 (Separator)

## Slide 11
RI beam
Primary beam
Beam dump
Production target
Slit
Slit
Bending magnet
Bending magnet
Momentum dispersive focal plane
Position measurement
Energy loss/Time-of-flight measurements
Momentum dispersive focal plane
Achromatic focal plane
Lorentz force: F = qvB
Centripetal force: F = mv2/ρ2
mv/q = Bρ ~ horizontal position
Velocity v = Flight length / TOF
Nuclear charge Z ~ ΔE1/2 v
Achromatic focal plane
Position measurement → determine mv/q
Position and TOF measurements → determine A/q
Energy loss/Time-of-flight measurements → determine Z
Bρ- ΔE-TOF method
Basics of Seperator : 2차 빔 분리 장치 (Separator)

## Slide 12
Quadrupole Magnet: 4극 전자석
Ion beam
Horizontally focused
Vertically defocused
Horizontally defocused (weak)
Vertically focused (strong)
From KR tech
From KR tech
Ion beam
High momentum ion
Low momentum ion
S
N
Bending magnet (dipole magnet: 2극 전자석)
Including momentum spread
This horizontal size corresponds to the momentum dispersion.
B = 0 for center
Example
Example
4극 2극 전자석

## Slide 13
Korea Broad acceptance Recoil spectrometer and Apparatus
SCL3
SCL2
Stage1
Stage2
(Future extension)
KoBRA Stage1
Stage1:
  RI beam productions at a few MeV/u or at about 20 – 40 MeV/u using a stable beams for study of nuclear astrophysics and nuclear structure
  Recoil mass separator (with Stage2) at about less than few MeV/u for direct measurements of radiative-capture cross sections
Stage2 (Future extension, Detailed concept is under discussion with RAON Users Association):
  High resolution separator (where Stage1 is used as a dispersion matching section)
  Recoil mass separator (with Stage1) at about less than few MeV/u for direct measurements of radiative-capture cross sections
Curved edge bending magnet
Future plan

## Slide 14
Korea Broad acceptance Recoil spectrometer and Apparatus
CRIB/CNS
SECAR/MSU
RI beam production for study of nuclear astrophysics in the energy of few MeV/u like CRIB.
Recoil spectrometer for study of nuclear astrophysics in the energy of < few MeV/u like SECAR or DRAGON.
RIPS/RIKEN
After adding Stage2,
RI Beams from ISOL facility
RI beam production for studies of nuclear structure & nuclear reaction in the energy of 20 – 40 MeV/u for A < about 40 like RIPS.
Magnetic rigidity | 0.25 – 3.0 Tm
Angular acceptance | 80 mrad (H) 200 mrad (V)
Momentum acceptance | 8%
Momentum resolving power at F1 | 2100 at 2 mm beam size
Mass resolving power (with Wien filter) | 1000 at 2 mm beam size
Beam swinger | up to 12 degree for 3 Tm
High order correction | up to 4th order
Degrader at F1 | Homogeneous
Specification of KoBRA stage1
TRIUMF

## Slide 15
 | RIBLL (HIRFL) | RIPS (RIKEN) | CRIB (CNS, University of Tokyo) | KoBRA stage1 (RAON)
Layout |  |  |  | 
Magnetic Rigidity | ≤ 4.2 Tm | ≤ 5.8 Tm | ≤ 1.3 Tm | 0.25 – 3.0 Tm
Separator Length | 35 m | 28 m | About 13 m | 38 m
Energy Acceptance | 20% | 12% | 30% | 16%
Angular Acceptance | 50 mrad | 80 mrad | 75 mrad | 80 mrad (H), 200 mrad (V)
Incl. Wien Filter | No | No | 1.5 m (50 kV/cm) | 2.5 m (27 kV/cm)
Beam Swinger | Up to 5° | Up to 15° | Rotatable separator (-5°−60°) | Up to ±12°
Z. Sun et al., NIM A 503 (2003) 496, T. Kubo et al., NIM B 70 (1992) 309, Y. Yanagisawa et al., NIM A 539 (2005) 74, K. Tshoo et al., NIM B 376 (2016) 188.
Specification comparison chart of RI beam Separators
Secondary beam envelope of KoBRA stage1 & PID spectrum simulated
5th order ion optics
5th order ion optics
48Ca beam (35 MeV/u), 9Be target

## Slide 16
 | DRAGON (TRIUMF) | SECAR (MSU) | KoBRA stage1 (RAON) | KoBRA stage1 + stage2 (RAON)
Layout |  |  |  | Improve a mass resolution & primary beam rejection with cleanup section (Under Discussion)
Magnetic Rigidity | ≤ about 0.6 Tm | 0.14 − 0.8 Tm | 0.25 – 3.0 Tm | 
Max. Electric Rigidity | ≤ 8.0 MV | 1.0 − 19.0 MV | 2.0 − 18.5 MV | 
Spectrometer Length | 21 m | About 40 m | 38 m | 
Angular Acceptance | 40 mrad (H), 50 mrad (V) | 50 mrad | 80 mrad (H), 200 mrad (V) | 
Energy Acceptance | 10% | 6.2% | 16% | 
Mass Resolution | ≈ 350 | ≈ 750 | ≈ 650 | 
Primary Beam Rejection | About 10−13 | 10−13 −10−14 | > ~10−13 | 
D.A. Hutcheon et al., NIM A 498 (2003) 190, J.M. D’Auria, Nucl. Phys. A 701 (2002) 625c, G.P.A. Berg et al., NIM A 877 (2018) 87.
Specification comparison chart of recoil mass spectrometers
Position distribution at F3 (mm)
Simulated trajectories of primary bream and recoil product for KoBRA stage1
1.85 MeV/u 65As (0.6 Tm) with H gas target
Charge selection
Mass selection
WF
WF

## Slide 17
Design History of KoBRA
Stage1
Stage2
Year 2012.07 – 2014.04
Only optical design
Unrealistic multipole magnets
Unrealistic drift spaces
Year 2011.12
Rare Isotope Science Project (RISP) Launched
Year 2011.12 – 2012.06
Only optical design
Unrealistic multipole magnets
Unrealistic drift spaces
Adding High resolution separator function
KoBRA was divided into two stages, stage1 and stage2
Adding multipole magnets
(6 sextupoles, 2 octupoles for stage1 )
Increasing Magnetic Rigidity
(1.5 Tm → 3 Tm)
Year 2014.05 – 2015.02
RI beam production at a few MeV/u
Recoil mass spectrometer
RI beam production at a few MeV/u
Recoil mass spectrometer
High resolution separation
Adding RI beam production at few tens MeV/u
Increasing angular acceptance
(40 mrad → > 80 mrad)
Decreasing energy acceptance
(20% → 16%)
Starting Magnet design
RI beam production at a few MeV/u
RI beam production at < 40 MeV/u
Recoil mass spectrometer
High resolution separation
Adopting curved edge bending magnets
Removing all multipole magnets
Designing all of magnets
Reflecting the field maps of designed magnets
Year 2015.03 – 2016.07
Realistic magnet design
Reasonable drift spaces
Realistic magnet design
Reasonable drift spaces
Comments from 2nd KoBRA Review Meeting were reflected
Final design of stage1
Adding a Swinger magnets
Adding a two sextupoles
Redesigning bending magnet
Designing diagnostic chambers
Redesigning radiation shielding walls
Accommodating a space for concrete wall
Stage2 is under discussion
Year 2016.08 – 2017.04
Year 2017.05 – 2018.04
Base line Design Summary
2012.06
2013.06
Technical Design Report
1st KoBRA review meeting
2014.02
2015.08
KoBRA mini workshop
2016.08
2nd KoBRA review meeting
Stage1
2018.05
RAON Users Association lunched
2011.12
RISP lunched
Now stage1 is being produced with international/domestic companies
Year 2018.05 – present
Only optical design
Unrealistic multipole magnets
Unrealistic drift spaces
Purchasing procedures
Bidding excluding Wien filter

## Slide 18
Present Status (Separator)
Contracted on April 2018
(Korea)
Productions of quadrupole and sextupole magnets
(Danmark)
Project management
Designs of all magnets
Productions of bending magnets and swinger
(Korea)
Project management
Consortium
(Korea)
Designs and productions of diagnostic chambers, beam pipe, beam dump, and etc
Large quadrupole magnet
Small quadrupole magnet
Swinger
Sextupole magnet
F1 chamber
F2 chamber
F3 chamber
F0
F1
F2
F3
Wien Filter will be added later due to the limitation of budget.
Contracted on December 2018
Removable scattering chamber
Empty space for Si-detector array
or IC chamber
5 m

## Slide 19
All of detectors are fulfilled KoBRA detection system requirements.
Complete KOBRA detection system including spare detectors, Ion Chamber, HPGe gamma array and DAQ system will be ready by the middle of 2019.
PPACs
We have six 10 x 10 cm2, two 20 x 20 cm2, two 40 x 20 cm2 active area PPACs
Position resolution: < 1 mm in FWHM, (C4H10 gas, 16O beam at 2x106 pps )
SSD
We have two 5 x 5 cm2 active area, 50 m-thick, 16 channel SSD
Energy resolution ~ 0.7%, S/N ~ 272 for 5.486 MeV  in vacuum
Plastic scintillator detectors
We have one 10 x 10 cm2 active area, 100 m thick both side readout plastic detector
Time resolution < 42 ps for 5.486 MeV  in vacuum
One 10 x 10 cm2 active area, 100 m thick one side readout plastic will be produced
Present Status (Detectors)
HPGe gamma ray detectors
32 segmented HPGe detectors (6set)
Compton suppressor BGO crystals (6set)
Complete set of TIGRESS electronics
Large area PPACs
PPACs
SSD
PPACs
Plastic detector
HPGe gamma array
* Charles Akers et al., NIM A In Press, Accepted Manuscript (2018)
4th RISP SPAC 1- 2 April 2019

## Slide 20
Present Status (photos of Low Energy Experimental Hall)
12 March, 2019
15 March, 2019
15 March, 2019
E1 (KoBRA)
E2
E3
Low Energy Experimental Hall B (Neutron science)
Low Energy Experimental Hall A
Beam Transport Room 1
Low Energy Experimental Hall B (Neutron science)
E1 (KoBRA)
SCL3
SCL3 Tunnel
SCL2 Tunnel
The finishing materials of Low Energy Experimental Hall will be completed till the end of 2019.
Utility to supply electric power, cooling water, and air conditioning for Low Energy Experimental Hall A will be ready till the end of 2020.
4th RISP SPAC 1- 2 April 2019

## Slide 21
Present Status (Separator)
F0
F1
F2
F3
Curved edge bending magnet 총 2기 공장검사 (성능시험) 중 (‘20.07.15)
Small quadrupole magnet 총 8기 저에너지실험동A에 입고 완료 (‘20.06.22)
Sextupole magnet 총 2기 저에너지실험동A에 입고완료 (‘20.06.22)
Swinger magnet 1 and 2 저에너지실험동A에 입고완료 (’20.05.08)
2020.04.
2020.04.
2020.04.
2020.01.
Large quadrupole magnet 총 7기 공장검사 중 (‘20.07.15)
F1/F2/F3 빔진담 진공챔버 공장검사 완료 및 입고준비 중 (‘20.07.15)
빔덤프 공장검사 완료 및 입고 준비 중 (‘20.07.15)

## Slide 22
KOBRA
3. Sys. Install.
• We plan to complete the installation of KoBRA till the end of this year, and to perform the commissioning with stable ion beams from the beginning of next year (2021).
2020.04.
2020.04.
Water cooled collimator
Water cooled Beam dump
2015
High power target (Prototype)
Particle detector system
2020.04.
Installation test of radiation shielding blocks (Low Energy Experimental Hall A)
2020.04.03
2020.04.09
2020.04.20

## Slide 23: Scientific program at early phase operation(candidate)
Facility | Subject for early phase operation
KOBRA | ∙ Transfer reaction measurements in inverse kinematics (29P(d,p)30P, 26Al(a,p)24Si) ∙ Radiative capture reactions using batch mode RI beams (26gAl(p,g)27Si) ∙ RI beam production via quasi-projectile-like fragmentation for 16O or 40Ar
LAMPS | ∙ Ar+KCl or Xe+CsI in case of IF separator commissioning not completed
MMS | ∙ Isomer separation with using 26g.s.Al and 26mAl beams
CLS | ∙ Laser ionization and measurement of isomeric property for 26Al
NDPS | ∙ Activation experiments with a quasi mono energy neutrons for light and heavy nuclei ∙ Surrogate reactions for fission
mSR | ∙ One of research areas of superconductivity and quantum magnetism with their scientific significance at the time of the μSR instrument completion
BIS | ∙ Physical dose distribution and linear energy transfer measurements with a 12C+6 beam (310 MeV/u)
3. Sys. Install.

## Slide 24
Physics topic (long term plan)
One of the major goals @ KoBRA: to understand the origin of the chemical elements (Nuclear Astrophysics)
• Direct measurements of charged-particle induced (p,g) and (a,g) radiative capture reactions
e.g. 65As(p,g)66Se and 15O(a,g)19Ne reactions at Ebeam < ~ 1 MeV/nucleon
• Transfer reaction measurements for single-particle and single-hole state studies at the beam energy of about a few MeV/nucleon
• Measurements of excitation functions for astrophysically-important compound nucleus reactions such as (p,a) and (a,p)
• elastic & inelastic scattering measurements in inverse kinematics using 1H and 4He targets
Massive stars (WR, AGB)
T < 0.1 GK
Novae
T < 0.6 GK
Core-collapse supernovae
T ~ 3 GK
Constraining reaction rates over large temperature range is required!

## Slide 25
Physics topic (short term plan)
Candidate for early stage RIBs at KoBRA
can be produced at ISOL facility
can be produced using batch mode sputter ion source
can be produced at KOBRA
18F
26gAl
29P
26gAl (t1/2 = 7.2*105 y)
• dry material sample
→ dissolving in HCl
→ compressed into a pellet
→ Cs sputter ion source
• 26gAl(d,p)27Al reaction
(for 68- and 127-keV resonance)
29P (t1/2 = 4.142 s)
• KoBRA, production mode
• 40Ar primary beam on 9Be target
• 29P(d,p)30P measurement for the 26Al(a,p)24Si reaction rate
18F (t1/2 = 109 min)
• high intensity a beam from the cyclotron and
HfO2 ISOL target
• through the 16O(a,pn)18F reaction
• 18F(p,a)15O reaction (for the 330 keV resonance)

## Slide 26
Anticipated early phase experiment: 18F + p
Isotope | Lifetime | Decay process | g-ray produced | Nova type
13N | 0.24h | b+-decay | 511 keV + cont. | CO & ONeMg
18F | 2h | b+-decay | 511 keV + cont. | CO & ONeMg
7Be | 77d | e--capture | 478 keV line | CO
22Na | 3.75y | b+-decay | 1275 keV + 511 keV | ONeMg
26Al | 106y | b+-decay | 1809 keV + 511 keV | ONeMg
INTEGRAL
(ESA, 2002)
18F(p,a)15O
• direct measurements:
Bardayan (2002), Chae (2006), Sereville (2009), Beer (2011)
• many indirect measurements
18F(p,g)19Ne: measured only one time by Akers (2013)
Bardayan et al. (2002)
Chae et al. (2006)
Beer et al. (2011)
330 keV resonance
In the 18F + p system (19Ne)

## Slide 27
Anticipated early phase experiment: 26Al(d,p)27Al
1.809 MeV
26Al(p,g)27Si reaction through 68- and 127-keV resonance

## Slide 28
Anticipated early phase experiment: RIB production
RI beam production via quasi-projectile-like fragmentation from 16O or 40Ar in the energy range of 20 – 30 MeV/u with a light mass target
We consider a measurement of the production cross section using commissioning beams, such as 16O and 40Ar, delivered from SCL3 with a 9Be or 12C production target, in the early part of 2021 due to the lack of production cross section data in the energy range of 20 - 30 MeV/u.
We believe that such experiment can give us not only the commissioning results but also the some guide lines of available RI beams for the future experiments.
RI beam intensity for 100 pnA 16O beam with 0.3 mm-thick 12C target
RI beam intensity for 100 pnA 40Ar beam with 0.3 mm-thick 12C target
Cross section: EPAX2
Cross section: EPAX2
KoBRA LISE++
LISE++
16O primary beam
Beam dump
We distributed LISE++ file to domestic users. LISE++ is useful to easily understand spectrometer tuning for beginners and to presume the intensity of secondary beam.

## Slide 29
Future Plan (under discussion)
RIBs from ISOL
HPGe Detector & Gas jet target
4th RISP SPAC 1- 2 April 2019
Cross section measurements for
Radiative capture reactions (p,g) & (a,g) at A > ~30
Wien filter
Wien filter
Cross section measurements for
Radiative capture reactions (p,g) & (a,g) at A < ~30
Fast ionization chamber
Silicon detector array

## Slide 30
Present Human resources for KoBRA
Activity | Name | Note
Managing development (KoBRA & NDPS) | Dr. K.Tshoo | RISP
Development of KoBRA separator | Dr. K.Tshoo | RISP
Interface between building utilities and KoBRA | Mr. S.J.Pyeun | RISP
Large & small area PPACs development | Dr. K.B. Lee, Dr. C. Akers | RISP
Silicon detector development | Dr. K.B. Lee | RISP
Plastic detector development | Dr. E.H. Kim | RISP
HPGe detectors & DAQ developments | Dr. J.H. Park, Dr. K.B. Lee | RISP KEK-KISS group
Remote control system development | Dr. M. Kim, Mr. S.J.Pyeun | RISP
Local control system of beam dump and NMR probe | S.J.Pyeun, Prof. Y.K. Kim, Dr. J. Park | RISP, Hanyang University
Ion optics for KoBRA, in particular radiative capture mode | Prof. G.P.A. Berg | University of Notre Dame
Nuclear reaction models for RI beam production | Prof. G.A. Souliotis | University of Athens
Design concept of separator and magnets | Prof. S. Kubono Prof. S. Kato | RIKEN Yamagata University
Early phase & Day1 experiments, Development of ion chamber detector | Prof. K. Chae, Mr. M.S. Kwag | SungKyunKwan University
Early phase & Day1 experiments, Development of silicon detector array | Prof. K. I. Hahn, Dr. D.H. Kim | Ewha Womans University
Early phase & Day1 experiments | Prof. C.-B. Moon Prof. S. Choi Prof. H.K. Park, Prof. J.B. Bahng | Hoseo University Seoul National University Korea University
4th RISP SPAC 1- 2 April 2019

## Slide 31
Budget & Schedule for KoBRA
Item | Budget
KoBRA separator (magnets, power supplies, vacuum system, beam dump system, cable tray and so on) | 7078 MKRW (6.3 MUSD)
Production target system (rotating target) | 235 MKRW (0.21 MUSD)
Detector system (detectors with electronics and DAQ) | 7273 MKRW (6.5 MUSD)
Remote control system (slow control system based on PLC) | 468 MKRW (0.42 MUSD)
Total | 15054 MKRW (13.43 MUSD)
KoBRA construction Schedule
Budget

## Slide 32
Summary
Multi-purpose experimental instrument KoBRA has been designed for about six years after the RISP was established, and Stage 1 is currently under construction.
KoBRA stage1 was designed not only for the RI beam productions but also for direct measurements of radiative-capture cross sections in the astrophysical energy range.
Stage2 would be used to improve both mass resolution and primary beam rejection, but it is still under discussion.
Construction of stage1 will be completed by the end of 2020, and early phase experiment will be performed in 2021, but the topic is under discussion.
We expect that KoBRA will give an opportunity to study astrophysically interesting reactions in the future, as well as the nuclear structure of exotic nuclei in the energy range of 10-30 MeV/nucleon.
4th RISP SPAC 1- 2 April 2019

## Slide 33
KoBRA Collaborators
Hanyang University
  Y.K. Kim, J. Park
Seoul National University
  S. Choi, H. Chae (student)
Sungkyunkwan University
  K. Chae, M.S. Kwag (student)
Ewha Womans University
  K. I. Hahn, D.H. Kim, S. Lim, J.Y. Huh
Hoseo University
  C.-B. Moon
Korea University
  H.K. Park, J.B. Bahng
RIKEN Nishina Center
  S. Kubono
Yamagata University
  S. Kato
National and Kapodistrian University of Athens and Hellenic Institute of Nuclear Physics
  G.A. Souliotis
University of Notre Dame
  G.P.A. Berg
KEK-KISS group
Domestic collaborators
International collaborators
4th RISP SPAC 1- 2 April 2019

## Slide 34
Thank you very much for your kind attention
4th RISP SPAC 1- 2 April 2019